# ESP8266(LiLon NodeMCU V3)
## Get started
Arduino setup (from https://www.instructables.com/id/Getting-Started-With-ESP8266LiLon-NodeMCU-V3Flashi/)
1. File → Preferences…
2. Additional Boards Manager URL: http://arduino.esp8266.com/stable/package_esp8266com_index.json
   OK
3. Tools → Boards → Boards Manager
4. Search: esp8266
   Install
5. Tools → Boards → NODEMCU 1.0 (ESP - 12E Module)

## Pin usage

GPIO Pin	I/O Index Number	Label	Input	Output
GPIO0	3	D3	pulled up	OK	connected to FLASH button, boot fails if pulled LOW
GPIO1	10	TX	TX pin	OK	HIGH at boot, debug output at boot, boot fails if pulled LOW
GPIO2	4	D4	pulled up	OK	HIGH at boot connected to on-board LED, boot fails if pulled LOW
GPIO3	9	RX	OK	RX pin	HIGH at boot
GPIO4	2	D2	OK	OK	often used as SDA (I2C)
GPIO5	1	D1	OK	OK	often used as SCL (I2C)
GPIO6	N/A
GPIO7	N/A
GPIO8	N/A
GPIO9	11
GPIO10	12
GPIO11	N/A
GPIO12	6	D6	OK	OK	SPI (MISO)
GPIO13	7	D7	OK	OK	SPI (MOSI)
GPIO14	5	D5	OK	OK	SPI (SCLK)
GPIO15	8	D8	pulled to GND	OK	SPI (CS) Boot fails if pulled HIGH
GPIO16	0	D0	no interrupt	no PWM or I2C support	HIGH at boot, used to wake up from deep sleep
ADC0		A0	Analog input	X

Use either D-number, ie “D0”, or GPIO-number, ie “16”
## Test code
will create a web page to set an LED
#include <ESP8266WiFi.h>
const char* ssid = "Magesh";
const char* password = "jayakumar";
int ledPin = 13; // GPIO13
WiFiServer server(80);
void setup() {
Serial.begin(115200);
delay(10);
pinMode(ledPin, OUTPUT);
digitalWrite(ledPin, LOW);
// Connect to WiFi network
Serial.println();
Serial.println();
Serial.print("Connecting to ");
Serial.println(ssid);
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println("");
Serial.println("WiFi connected");
// Start the server
server.begin();
Serial.println("Server started");
// Print the IP address
Serial.print("Use this URL to connect: ");
Serial.print("http://");
Serial.print(WiFi.localIP());
Serial.println("/");
}
void loop() {
// Check if a client has connected
WiFiClient client = server.available();
if (!client) {
return;
}
// Wait until the client sends some data
Serial.println("new client");
while(!client.available()){
delay(1);
}
// Read the first line of the request
String request = client.readStringUntil('\r');
Serial.println(request);
client.flush();
// Match the request
int value = LOW;
if (request.indexOf("/LED=ON") != -1) {
digitalWrite(ledPin, HIGH);
value = HIGH;
}
if (request.indexOf("/LED=OFF") != -1) {
digitalWrite(ledPin, LOW);
value = LOW;
}
// Set ledPin according to the request
//digitalWrite(ledPin, value);
// Return the response
client.println("HTTP/1.1 200 OK");
client.println("Content-Type: text/html");
client.println(""); // do not forget this one
client.println("<!DOCTYPE HTML>");
client.println("<html>");
client.print("Led pin is now: ");
if(value == HIGH) {
client.print("On");
} else {
client.print("Off");
}
client.println("<br><br>");
client.println("<a href=\"/LED=ON\"\"><button>Turn On </button></a>");
client.println("<a href=\"/LED=OFF\"\"><button>Turn Off </button></a><br />");
client.println("</html>");
delay(1);
Serial.println("Client disonnected");
Serial.println("");
}